## Slide 1: Important Fuels used in Hotel Kitchens

## Slide 2
The fuels are: 1. LPG 2. CNG 3. Coal 4. Wood 5. Electricity 6. Steam 7. Solid Fuel/ Handy Fuel 8. Solar Energy.

## Slide 3: Fuel # 1. LPG:
LPG or liquefied petroleum gas is the generic name for commercial propane and butane composed fuel used in the kitchen to fuel gas burners. This gas is supplied in industrial cylinders or in bulk storage tanks at the hotel premises. It is supplied to the hotel kitchen through pipelines.
The LPG cylinders are stored in a separate place, usually known as. ‘Gas bank’ and are usually operated by a department in the hotel called ‘kitchen stewarding’. Amount of gas cylinders used in the gas bank depends on the types of operations they are used for.
A large hotel may have more than 100 cylinders. Half of these would be installed to supply gas whereas half would always be a backup. A certain gas pressure is maintained by the stewarding department as certain ranges require high pressure for cooking. LPG is liquefied under pressure and converts into gas when the pressure is released.

## Slide 4
It is almost smokeless and easy to handle. LPG should be handled with utmost care as being a transparent gas its leakage is not easily detectable and it is also highly combustible.
There are certain government regulations regarding the usage of LPG. For example, LPG cannot be used in basement kitchens or below the sea level and hence, in those kinds of conditions one has to rely on electricity or steam- operated equipment.

## Slide 5: Usage:
It is one of the most essential fuels used in the hotel kitchen and is known for its efficiency. It is used as a fuel for cooking ranges, ovens, and salamanders. Some tandoors used in Indian cooking are also fired by LPG

## Slide 6: Fuel # 2. CNG:
Compressed natural gas is slowly gaining popularity for its fuel efficiency and environment-friendly properties.

## Slide 7: Usage:
It is used in eco-friendly hotels as fuel in many types of equipment such as ovens, gas ranges, etc.

## Slide 8: Fuel # 3. Coal:
Though it is a very crude form of fuel to be used in a modern kitchen, it is still very popular. The smoky flavour which the charcoal imparts is much desired. Coal should always be stored away from food area, ideally in a cool, dark room away from any moisture. Usually separate areas are built near the receiving area for coal storage as coal is combustible and messy.

## Slide 9: Usage:
Coal is used in a hotel kitchen to light tandoor and grills for barbecue. The coal used in the hotels is wood charcoal only.

## Slide 10: Fuel # 4. Wood:
One would have come across wood-fired pizza ovens in the modern restaurants today. Gaining popularity of pizzas has led to the origin of this oven which lends an aesthetic appearance to the restaurant, where chefs prepare pizzas in front of the guests. Though it is also operated by LPG, few logs of wood are placed inside to impart a smoky flavour to the pizzas.

## Slide 11: Usage:
It is used as a fuel for wood-fired pizza ovens. The pizza ovens have LPG fire but wood is also kept inside to impart a smoky flavour to the food.

## Slide 12: Fuel # 5. Electricity:
Electricity is also used as fuel to operate many types of equipment. Care should be taken while ordering such equipment as many countries operate on certain volts. In India equipment works on 220 volts, whereas in the USA equipment works on 110 volts. So care should be taken while importing equipment.
Some of the heavy duty equipment use three-phase electric current and some use only single phase. So it is important that the instructions are read before installing the new machinery.

## Slide 13: Usage:
Electricity is generally used to operate most of the equipment in the hotel kitchen. It is popular in the hotel kitchens because it is easy to control electrical equipment.

## Slide 14: Fuel # 6. Steam:
Most of the hotels produce steam, which is used to cook or operate equipment. Steam is supplied to the hotel kitchen through insulated pipes.
Usage:
Steam is used in equipment such as dishwashers and steam jacket kettles.

## Slide 15: Fuel # 7. Solid Fuel/ Handy Fuel:
This fuel is made from petroleum jelly and comes in small tins. These are mostly used in F&B service areas.
Usage:
This type of fuel is hardly used in hotel kitchens but is very commonly used in F&B service, where it is used in heating up food in the chafing dishes used commonly in banquets.

## Slide 16: Fuel # 8. Solar Energy:
The heat from the sun is used as a fuel. This is not a very commonly used fuel in the kitchens, but many eco- friendly hotels have solar cookers that are used in cooking.
Usage:
Solar cookers utilize solar energy to cook food.